## Slide 1: Towards Efficient Traffic Monitoring for Science DMZ with Side-Channel based Traffic Winnowing
Hongda Li, Fuqiang Zhang, Lu Yu, Jon Oakley, Hongxin Hu, and Richard R. Brooks
SDN-NFV Security 2018

## Slide 2: Outline
Introduction
Approach Overview
Lightweight Detection System Development
Evaluation

## Slide 3: Traditional High Performance Data Transfer
WAN
Campus LAN
Campus LAN
Data Servers
Data Servers
Campus Router/Firewall
Campus Router/Firewall

## Slide 4: Traditional High Performance Data Transfer
WAN
Campus LAN
Campus LAN
Data Servers
Data Servers
Campus Router/Firewall
Campus Router/Firewall
1.Inappropriate security policies
2.Low-performance general-purpose networks
4.Low-performance general-purpose data servers
3.Hard to monitor performance

## Slide 5: Science DMZ
WAN
Campus LAN
Campus LAN
High performance Data Transfer Nodes
High performance Data Transfer Nodes
Campus Router/Firewall
Campus Router/Firewall
Border Router
Border Router
Science DMZ Router
Science DMZ Router
Virtual/Dedicated Connection

## Slide 6: Threat Model
Border Router
WAN
Compromised Data Transfer Node
Malicious programs are installed and launched
Traffic monitoring to capture the anomalies
Science DMZ Router

## Slide 7: Tension Between Two Requirements
Border Router
WAN
Compromised Data Transfer Node
Malicious programs are installed and launched
Traffic monitoring to capture the anomalies
High-performance data transfer
  100 Gbps or higher
Low-performance traffic monitoring
  Snort with 800 Mbps per processor
  Bro with 80 Mbps per core

## Slide 8: Limitations of Existing Approaches
Improving the processing capacity of IDSes
  Multi-thread/core IDSes
  Cluster-based IDSes
  Special hardware IDSes
Notes: Recently, there are two emerging network technologies. NFV and SDN.
IDS can be virtualized to run on virtual machines that can be dynamically created, destroyed or migrated, which provides more elasticity.
Some existing works, like split/merge and OpenNF, have studied dynamic state management for virtualized network functions.
Unfortunately, all these existing works treat a virtualized IDS as a monolithic piece of software, where components within one virtualized IDS cannot run independently.
The nature of monoliths make the distribution of virtualized IDS into cloud-based systems with significant limitations.

## Slide 9: Limitations of Existing Approaches
Improving the processing capacity of IDSes
  Multi-thread/core IDSes
  Cluster-based IDSes
  Special hardware IDSes
Devoting more resources
Notes: Recently, there are two emerging network technologies. NFV and SDN.
IDS can be virtualized to run on virtual machines that can be dynamically created, destroyed or migrated, which provides more elasticity.
Some existing works, like split/merge and OpenNF, have studied dynamic state management for virtualized network functions.
Unfortunately, all these existing works treat a virtualized IDS as a monolithic piece of software, where components within one virtualized IDS cannot run independently.
The nature of monoliths make the distribution of virtualized IDS into cloud-based systems with significant limitations.

## Slide 10: Limitations of Existing Approaches
Improving the processing capacity of IDSes
  Multi-thread/core IDSes
  Cluster-based IDSes
  Special hardware IDSes
Tuning the IDSes based on traffic pattern
  Predicting the traffic pattern
Devoting more resources
Notes: Recently, there are two emerging network technologies. NFV and SDN.
IDS can be virtualized to run on virtual machines that can be dynamically created, destroyed or migrated, which provides more elasticity.
Some existing works, like split/merge and OpenNF, have studied dynamic state management for virtualized network functions.
Unfortunately, all these existing works treat a virtualized IDS as a monolithic piece of software, where components within one virtualized IDS cannot run independently.
The nature of monoliths make the distribution of virtualized IDS into cloud-based systems with significant limitations.

## Slide 11: Limitations of Existing Approaches
Improving the processing capacity of IDSes
  Multi-thread/core IDSes
  Cluster-based IDSes
  Special hardware IDSes
Tuning the IDSes based on traffic pattern
  Predicting the traffic pattern
Devoting more resources
Lack of dynamics
Notes: Recently, there are two emerging network technologies. NFV and SDN.
IDS can be virtualized to run on virtual machines that can be dynamically created, destroyed or migrated, which provides more elasticity.
Some existing works, like split/merge and OpenNF, have studied dynamic state management for virtualized network functions.
Unfortunately, all these existing works treat a virtualized IDS as a monolithic piece of software, where components within one virtualized IDS cannot run independently.
The nature of monoliths make the distribution of virtualized IDS into cloud-based systems with significant limitations.

## Slide 12: Limitations of Existing Approaches
Improving the processing capacity of IDSes
  Multi-thread/core IDSes
  Cluster-based IDSes
  Special hardware IDSes
Tuning the IDSes based on traffic pattern
  Predicting the traffic pattern
SciPass
  Totally bypassing IDSes
Devoting more resources
Lack of dynamics
Notes: Recently, there are two emerging network technologies. NFV and SDN.
IDS can be virtualized to run on virtual machines that can be dynamically created, destroyed or migrated, which provides more elasticity.
Some existing works, like split/merge and OpenNF, have studied dynamic state management for virtualized network functions.
Unfortunately, all these existing works treat a virtualized IDS as a monolithic piece of software, where components within one virtualized IDS cannot run independently.
The nature of monoliths make the distribution of virtualized IDS into cloud-based systems with significant limitations.

## Slide 13: Limitations of Existing Approaches
Improving the processing capacity of IDSes
  Multi-thread/core IDSes
  Cluster-based IDSes
  Special hardware IDSes
Tuning the IDSes based on traffic pattern
  Predicting the traffic pattern
SciPass
  Totally bypassing IDSes
Devoting more resources
Lack of dynamics
Lack of visibility after bypassing
Notes: Recently, there are two emerging network technologies. NFV and SDN.
IDS can be virtualized to run on virtual machines that can be dynamically created, destroyed or migrated, which provides more elasticity.
Some existing works, like split/merge and OpenNF, have studied dynamic state management for virtualized network functions.
Unfortunately, all these existing works treat a virtualized IDS as a monolithic piece of software, where components within one virtualized IDS cannot run independently.
The nature of monoliths make the distribution of virtualized IDS into cloud-based systems with significant limitations.

## Slide 14: Overview of Our Approach
Border Router
WAN
OpenFlow switch
Virtualization Platform
…
Dynamically adapting to load variations
Lightweight Detection System
Continuous monitoring
Update flow rules
Filtered Traffic
Reflected Traffic
IDS Instances
High Performance Data Transfer Nodes

## Slide 15: Lightweight Detection System Requirements
Very low false negative rate
  Malicious traffic is rarely considered as benign
  Benign traffic can be considered as malicious
Efficient detection
  Process each packet faster
  Analyze only a small portion of traffic to filter
Notes: Note that I use the term “rarely” here. This means, false negative rate can be tuned depending on the performance requirement. Usually, we set the false negative rate lower, the false positive rate is higher. So more less traffic is filtered out by the lightweight detection system. And more traffic will be delivered to the IDS instances. In an extreme case, the false negative rate is 0, and the false positive rate is 100%. Then all the traffic is delivered to the IDS instances. Effectively achieving 0 false negative rate is still an open issue of the anomaly based IDS.
However, the lightweight detection system can tolerate a relatively high false positive rate, because the IDS instances will further analyze the falsely classified traffic and provide more precise detection results.
For example, in our experiment, the lightweight detection system processes a packet in every 0.66 microsecond, while the Bro IDS instances process a packet in every 44 microseconds.

## Slide 16: Insight #1 of Science DMZ
Domain-specific applications
  Lustre/GPFS (high-speed parallel file system)
  GridFTP/FTD (high-speed data transfer)
  XRootD (discipline-specific tools)

## Slide 17: Insight #1 of Science DMZ
Domain-specific applications
  Lustre/GPFS (high-speed parallel file system)
  GridFTP/FTD (high-speed data transfer)
  XRootD (discipline-specific tools)
Baseline of what traffic should be deemed as benign

## Slide 18: Insight #1 of Science DMZ
Domain-specific applications
  Lustre/GPFS (high-speed parallel file system)
  GridFTP/FTD (high-speed data transfer)
  XRootD (discipline-specific tools)
Baseline of what traffic should be deemed as benign
Model of benign traffic
Side-Channel Analysis

## Slide 19: Modeling Network Protocols
Network protocol modeling via Hidden Markov Models (HMMs)
  C. Lu, et al. “A normalized statistical metric space for hidden markov models.”
  L. Yu, et al. “Inferring statistically significant hidden markov models.”
  X. Zhong, et al. “Side channel analysis of multiple pmu data in electric power systems.”
It’s been proved feasible to model the network protocol by time intervals of packets

## Slide 20: Insight #2 of Science DMZ
Elephant flows
  Size of flows is huge
  Duration of flows is long

## Slide 21: Insight #2 of Science DMZ
Elephant flows
  Size of flows is huge
  Duration of flows is long
Sufficient observation to infer HMMs for each flow
Relatively “small” portion of traffic to analyze

## Slide 22: Lightweight Detection System Design
Offline Training
Symbol Table
HMMs
Online Detection
Incoming Traffic
Flow Rule Management
Detection Results
Flow Rule Update

## Slide 23: Offline Training Process
Traffic Capturing
Extracting Time Intervals
Symbolization
Inferring HMMs
Symbol Table
HMMs

## Slide 24: Online Detection Process
Traffic Capturing
Extracting Time Intervals
Symbolization
Inferring HMMs
Packet Acquisition
Compute Time Interval
Assign Symbol
Count Probability of each Symbol
Symbol Table
HMMs
Chi-square test
Benign
Malicious
Not matched
Matched
Sufficient sampling
Insufficient sampling

## Slide 25: Evaluation
The processing time of each packet
  Lightweight detection system
  IDS instances
  Expectation of the hybrid of two
False positive rate lightweight detection system
Notes: We assume there is no statistic difference between the sizes of malicious traffic flows and benign traffic flows.

## Slide 26: Evaluation Setup
Data Collection
  GridFTP (benign) vs. SCP (malicious)
  Each flow transfers 10GB data
  Generated through VMs on CloudLab at Clemson
System Configuration
  Implement lightweight detection system
  Bro as IDS instances
Notes: We assume there is no statistic difference between the sizes of malicious traffic flows and benign traffic flows.

## Slide 27: Processing Time of Each Packet
T: expectation of processing time of each packet
L: processing time of lightweight detection system
I: processing time of IDS instances
: the ratio of traffic to analyze for filtering
: the ratio of malicious traffic
: false positive rate
Notes: We assume there is no statistic difference between the sizes of malicious traffic flows and benign traffic flows.

## Slide 28: Result Analysis
Parameters | Value
(Analysis ratio) | 0.1
(Malicious ratio) | 0.5
Tested Variables | Observed Value
L | 0.66 microsecond
I | 44.46 microseconds
 | 0.38
T | 32.7 microseconds
Notes: We assume there is no statistic difference between the sizes of malicious traffic flows and benign traffic flows.

## Slide 29: Result Analysis
Parameters | Value
(Analysis ratio) | 0.1
(Malicious ratio) | 0.5
Tested Variables | Observed Value
L | 0.66 microsecond
I | 44.46 microseconds
 | 0.38
T | 32.7 microseconds
Chart: Processing Time Per Packet (microsecond)
| LDS | IDS instance | Expectation
Processing Time | 0.66 | 44.46 | 32.7
Saved 26%
Notes: We assume there is no statistic difference between the sizes of malicious traffic flows and benign traffic flows.

## Slide 30: Result Analysis
Malicious ratio and FPR fixed
Analysis ratio and FPR fixed
Analysis ratio and malicious ratio fixed
Parameters | Value
(Analysis ratio) | 0.1
(Malicious ratio) | 0.5
(FPR) | 0.38
Decreasing any of this parameters will further reduce the expectation of processing time!
Notes: We assume there is no statistic difference between the sizes of malicious traffic flows and benign traffic flows.

## Slide 31: Conclusion and Future Work
Conclusion
  Present a new architecture for traffic monitoring in Science DMZ
  Demonstrate efficiency of side-channel based traffic winnowing
Future work
  Evaluate on real-world Science DMZ data
    More protocols
    More use scenarios
  Investigate more side-channel features
    Packet size, time interval deviations, etc.
  Employ advanced machine learning techniques
Notes:     diverse devices environment & device behaviors change rapidly

## Slide 32: Q & A
Thank you!

## Slide 33: Science DMZ
WAN
Campus LAN
Campus LAN
High performance Data Transfer Nodes
High performance Data Transfer Nodes
Campus Router/Firewall
Campus Router/Firewall
Border Router
Border Router
Science DMZ Router
Science DMZ Router

## Slide 34: Threat Model
Border Router
WAN
Compromised Data Transfer Node
Malicious programs are installed and launched

## Slide 35: Modeling Network Protocols
Network protocol modeling via Hidden Markov Models (HMMs)
  C. Lu, et al. “A normalized statistical metric space for hidden markov models.”
  L. Yu, et al. “Inferring statistically significant hidden markov models.”
  X. Zhong, et al. “Side channel analysis of multiple pmu data in electric power systems.”